## Slide 1
A NEW METHOD FOR MONAURAL SPEECH SEPARATION USING IBM
Guide: Dr. R. Rajavel, Associate Professor
Project by :
M. Naveen Narayanan - 312214106066
S. Somasundar - 312214106104
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING

## Slide 2: OUTLINE
Speech Separation
Objectives of the Project
Literature Survey
Weintraub Speech Separation System
Hardware and Software for Implementation
Graphical Results
Complexity Analysis
Work plan
Reference

## Slide 3: SPEECH SEPARATION
Speech separation is the process of separating the target speech signal from acoustic mixture
The acoustic mixture may be an another speech or environmental noise or both
Speech separation can be used in speech/speaker recognition, voice communication, air-ground communication, hearing aids, etc.
Various methods have been adopted for speech separation, mainly: Spectral Subtraction, Subspace analysis, Hidden Markov Modelling and Computational Auditory Scene Analysis

## Slide 4: CASA and IBM
CASA is the study of auditory scene analysis (ASA) by computational means
In essence, CASA systems are "machine listening” systems that mimic the human auditory system
The Ideal Binary Mask (IBM) has been proposed as a computational goal of CASA
IBM is basically a binary matrix, in which 1 indicates speech dominant T-F units and 0 indicated noise dominant T-F units
IBM is defined as
M(t,f) = 1 if s(t,f) – n(t,f) > 0,
0 Otherwise
where s(t,f) - target speech energy and
n(t,f) - interference energy in a T-F unit

## Slide 5: OBJECTIVES OF THE PROJECT
To implement the Weintraub speech separation system using Matlab
To implement the proposed speech separation system using Matlab
To compute and compare the computational complexity of these systems and show that the proposed system is less complex

## Slide 6: LITERATURE SURVEY
S.No | TITLE | AUTHORS | YEAR OF PUBLICATION | INFERENCE
1. | A theory and computational model of auditory monaural sound separation | M. Weintraub | 1985 | This research provides a complete analysis of the human auditory system. A conceptual approach was introduced to mimic the knowledge and information used by human auditory system to separate sounds. A computer model was developed to separate the speech of two simultaneous talkers
2. | A comparison of several computational auditory scene analysis (CASA) techniques for monaural speech segregation | Jihen Zeremdini, Mohamed Anouar Ben Messaoud and Aicha Bouzid | 2015 | This paper mainly focused on the different CASA stages and the IBM for monaural speech segregation. It describes the several methods that used CASA to separate composite speech such as Hu and Wang, Zhang and Liu, Zhao and Shao, Li and Guan approaches etc. Finally an evaluation and a comparison was presented for the different monaural speech segregation methods

## Slide 7: LITERATURE SURVEY
S.No | TITLE | AUTHORS | YEAR OF PUBLICATION | INFERENCE
3. | Time–Frequency Masking for Speech Separation and Its Potential for Hearing Aid Design | D.L. Wang | 2008 | This article introduces the T-F masking concept and reviews T-F masking algorithms that separate target speech from either monaural or binaural mixtures, as well as microphone-array recordings. This article also surveys recent studies that evaluate the perceptual effects of T-F masking techniques, particularly their effectiveness in improving human speech recognition in noise
4. | Frequency analysis and synthesis using a Gammatone filterbank | V. Hohmann | 2002 | This paper describes an efficient implementation of the 4th-order linear Gammatone filter based on an impulse-invariant, all-pole design. A linear auditory filter bank was constructed from these filters. This filter has been used in several applications involving computational auditory peripheral filtering

## Slide 8: LITERATURE SURVEY
S.No | TITLE | AUTHORS | YEAR OF PUBLICATION | INFERENCE
5. | Single Channel Speech Enhancement Using Ideal Binary Mask Technique Based on Computational Auditory Scene Analysis | Abrar Hussain, Kalaivani Chellappan, Siti Zamrat | 2016 | In this paper, ideal binary mask which is inspired by the computational auditory analysis is used to analyze and synthesize the input speech signals and masker signals in the time-frequency domain. Synthesized signals are evaluated for speech quality measurement in terms of segmental signal-to-noise ratio. This study uses Malay language based speech as input speech signals
6. | An Unsupervised Approach to Cochannel Speech Separation | Ke Hu and DeLiang Wang | 2013 | In this paper, an unsupervised method was proposed for cochannel speech separation. The proposed system uses the CASA algorithm for voiced speech segregation. The proposed system was compared with several other methods across a range of input SNR conditions

## Slide 9
Speech separation system proposed by Weintraub [Ref1]
For expanded diagram
WEINTRAUB SPEECH SEPERATION SYSTEM
Analysis
Filter
Bank
Computation of Ideal Binary
Mask
Synthesis
Filter
Bank
Mask
Multiplication
Noisy Speech
Resynthesized Speech

## Slide 10: HARDWARE and SOFTWARE REQUIRED
Personal Computer with MATLAB installed
To implement analysis and synthesis filter bank, compute IBM and demonstrate the process of speech separation

## Slide 11: RESULTS
Speech: “ The drip of the rain made a
pleasant sound”
Noise: Speech shaped noise
Length of speech signal = 22004 samples
Sampling Frequency = 8000Hz
SNR = 4db
Speech
Noisy Speech
Resynthesized Speech using Weintraub System

## Slide 12: GRAPHICAL RESULTS

## Slide 13: GRAPHICAL RESULTS

## Slide 14: GRAPHICAL RESULTS

## Slide 15: COMPUTATIONAL ANALYSIS
Length of Speech signal = 22004 samples
Length of the Impulse response in Gammatone Analysis and Synthesis Filter bank = 1024 samples
Number of Channels = 128
Number of Frames per channel = 275
The number of multiplications in Analysis Filter Bank = Length of Speech signal*Length of Impulse response*Number of Channels = 22004*1024*128 = 2884108288
The number of multiplications in the process of speech separation = Number of Channels*Number of Frames*Length of each Frame = 128*275*160 = 5632000
The number of multiplications in Synthesis Filter Bank = 22004*1024*128 = 2884108288

## Slide 16: WORKPLAN
 | AUG-2017 | SEP-2017 | OCT-2017 | NOV-2017 | DEC-2017 | JAN-2018 | FEB-2018 | MAR-2018
Literature Survey |  |  |  |  |  |  |  | 
Implementation of the existing system |  |  |  |  |  |  |  | 
Implementation of the proposed system |  |  |  |  |  |  |  | 
Comparing the Computational Complexity and Report Preparation |  |  |  |  |  |  |  | 

## Slide 17: REFERENCES
M. Weintraub, “A theory and computational model of auditory monaural sound separation,” Ph.D. dissertation, Dept. Elect. Eng., Stanford Univ., Stanford, CA, 1985
D.L. Wang, “Time–Frequency Masking for Speech Separation and Its Potential for Hearing Aid Design,” Trends in Amplification, Vol. 12, pp.332-353, December 2008
D.L. Wang, G.J. Brown, “Fundamentals of Computational Auditory Scene Analysis,” in Computational Auditory Scene Analysis, D.L Wang and G.J Brown, Wiley-IEEE Press, pp. 1-38, 2006

## Slide 18: REFERENCES
V. Hohmann, “Frequency analysis and synthesis using a Gammatone filterbank,” Acta Acustica united with Acustica, Vol. 88, pp. 433 – 442, January 2002
Jihen Zeremdini, Mohamed Anouar Ben Messaoud and Aicha Bouzid, “A comparison of several computational auditory scene analysis (CASA) techniques for monaural speech segregation”, Brain Informatics, Vol. 2, Issue 3, pp. 155 – 166, September 2015
Abrar Hussain, Kalaivani Chellappan and Siti Zamrat, ”Single channel speech enhancement using ideal binary mask technique based on computational auditory scene analysis”, Journal of Theoretical and Applied Information Technology, Vol. 91. No. 1, Semptember 2016

## Slide 19: REFERENCES
Belhedi Wiem, Ben Messaoud Mohamed Anouar, Bouzid Aichl, “Time-Frequency Masks for Monaural Speech Separation: A Comparative Review”, 7th International Conference on Sciences of Electronics, Technologies of Information and Telecommunications (SETIT), 2016
Ke Hu and DeLiang Wang, “An Unsupervised Approach to Cochannel Speech Separation”, IEEE Transactions on Audio, Speech and Language Processing, Vol.21, No.1, January 2013
N.Harish Kumar, R.Rajavel, “Monaural speech separation system based on optimum soft mask,” IEEE Int. Conf. on Computational Intelligence and Computing Research, 18-20 Dec 2014

## Slide 20
THANK YOU

## Slide 21: REFERENCES
V.A. Mane , Prof. Dr. S. B. Patil, ”Survey of Methods and challenges in Computational Auditory sense analysis”, International Journal of Innovative Research in Electrical, Electronics, Instrumentation and Control Engineering, Vol. 4, Issue 9, September 2016

## Slide 22
Proposed system to reduce computational complexity
PROPOSED SPEECH SEPERATION SYSTEM
Analysis
Filter
Bank
Computation of Ideal Binary
Mask
Synthesis
Filter
Bank
Mask Multiplication
Noisy Speech
Resynthesized Speech

## Slide 23: LITERATURE SURVEY
S.No | TITLE | AUTHORS | YEAR OF PUBLICATION | INFERENCE
7. | Time-Frequency Masks for Monaural Speech Separation: A Comparative Review | Belhedi Wiem, Ben Messaoud Mohamed Anouar, Bouzid Aichl | 2016 | This paper focusses the masking effect on Computational Auditory Scene Analysis (CASA) based systems for single channel speech separation (SCSS). The CASA system employed in this study is Hu and Wang model. The new proposed system uses a soft mask instead of the hard binary mask and they have proved that the soft mask provides a better separation quality.
8. | Monaural speech separation system based on optimum soft mask | N. Harish Kumar, R. Rajavel | 2015 | This paper proposes the optimum soft mask (OSM) to reduce the musical noise, by replacing the hard limiting weights of IBM with the variable weights. The Signal-to-Noise ratio is used as a measure to evaluate the performance of the proposed soft mask with the existing IBM in the context of monaural speech separation. The rest of the paper is organized in the following manner

## Slide 24: LITERATURE SURVEY
S.No | TITLE | AUTHORS | YEAR OF PUBLICATION | INFERENCE
9. | Survey of Methods and challenges in Computational Auditory sense analysis | V.A. Mane , Prof. Dr. S. B. Patil | 2016 | This paper is a study of various literature and methods that are used to solve the cocktail party problem. This paper discusses about the evolution of computational auditory scene analysis and the various steps taken to design and define the underlying process which will do human mimicry. The paper also describes about the challenges faced by CASA to segregate unvoiced speech from non speech interference